## Slide 1: Torque
Torque
Static Equilibrium

## Slide 2: Torque
Consider force required to open door. Is it easier to open the door by pushing/pulling away from hinge or close to hinge?
Farther from hinge, larger rotational effect!
close to hinge
away from hinge

## Slide 3: Torque
Torque, t , is the tendency of a force to rotate an object about some axis
  t is the torque
  r is the lever arm (or moment arm)
  F is the force
r
F
r
F

## Slide 4: Lever Arm
The lever arm, r, is the shortest (perpendicular) distance from the axis of rotation to a line drawn along the direction of the force
  r = L sin Φ
r

## Slide 5: Non perpendicular Torque
Only the y-component, Fsinf, produces a torque
F is the force
r is distance to point where F is applied
Φ is the angle between F and r

## Slide 6: Example 1
Two screwdrivers are available to a woodwork student who wishes to screw two pieces of wood together. The only difference between the two screwdrivers is that the handle is 3 cm wide on one and 1 cm wide on the other.
a. In order that the job be carried out with a minimum amount of effort, which screwdriver should the student select?
b If the force that is applied by the student is 45 N, determine the maximum torque that is delivered to the screw. [1.35 Nm]

## Slide 7: Example 2
Tessa has a mass of 60 kg and sits on a 6.0 m long seesaw so that her centre of mass is 1.25 m from the end. What torque does she produce? [1029 Nm anticlockwise]

## Slide 8: Example 3
The contents of a wheelbarrow produce a clockwise torque of 400 Nm about the wheel axle, which is 1.6 m from the end of the handles. If this wheelbarrow is to be wheeled away, what size force must be exerted? Assume the force acts 90  to the lever arm. [250 N]

## Slide 9: What if two or more different forces act on lever arm?

## Slide 10: Net Torque
The net torque is the sum of all the torques produced by all the forces
  Remember to account for the direction of the tendency for rotation
    Counterclockwise torques are positive
    Clockwise torques are negative

## Slide 11: Example 1:
Determine the net torque
Given:
weights: w1= 500 N
w2 = 800 N
lever arms: d1=4 m
d2=2 m
Find:
St = ?
500 N
800 N
4 m
2 m
N
1. Draw all applicable forces
2. Consider CCW rotation to be positive
Rotation would be CCW

## Slide 12: Translation Equilibrium
A body is said to be in translation equilibrium when the sum of the forces acting on a body is zero.
mg = 20 N
N = 20 N

## Slide 13: Rotational Equilibrium
For a body or system to be in Rotational equilibrium, the sum of all the torques acting about a point must be zero.

## Slide 14: Static Equilibrium
For a body or system to be in Static Equilibrium, it must be translation and rotational equilibrium
Σt = 0 and ΣF=0

## Slide 15: Where would the 500 N person have to be relative to fulcrum for zero torque?

## Slide 16: Example 2:
Given:
weights: w1= 500 N
w2 = 800 N
lever arms: d1=4 m
St = 0
Find:
d2 = ?
500 N
800 N
2 m
d2 m
N’
y
1. Draw all applicable forces and moment arms
According to our understanding of torque there would be no rotation and no motion!

## Slide 17: Example

## Slide 18: Example
While painting a tall building , a 70.0 kg painter stands 4.00 meter from the end of a 6.00 meter long plank that is supported by a rope at either end. The plank has a mass of 20.0 kg. Determine the tension in each rope

## Slide 19: Example
Cantilevers
Beam that extend beyond the base support
Used in structure that need to span some distance like bridges and diving boards
Entire weight of cantilever is supported by its support

## Slide 20: Example
An 8.00 m uniform ladder of weight 355N leans against a smooth vertical wall. A man whose weight is 875N , stands 6.30m from the bottom of the ladder. Find the forces that the wall and the ground exert on the ladder
500
8m
6.3m

## Slide 21
500
Fgy
Fgx
355N
875N
Fwall
355cos500
875cos500
Fwallsin500

## Slide 22: Struts and Ties
As well as the main beams and pillars, many structures have additional members that help to strengthen them. A structure may be supported by struts and ties

## Slide 23: Example